Pseudo-code for Checkpointing

Create a vector of states that will serve as checkpoints eg. [0, 4, 6,] Static vec for now

1. Run through simulation code ‘computeTrajectory’ for all time steps i
  1. After step next step i+1 is computed, only save the state ‘q[i-1]’ if the state is in the checkpoint array
    1. Use ‘q_i_temp’ to store these values one step at a time
  2. Save q[i_final]
2. Start with the Adjoint calculation going backward 1 step from q[i_final]
  1. Need q[i] → Load q[i_final]
  2. Need q[final-1]
    1. Rerun trajectory from most recent saved step eg [6]
    2. Save q[final-1]
  3. Compute Adjoint contribution
3. Add contribution to total derivative
4. For each subsequent step going backward:
  1. Need q[i] → Load the previous saved step q[final-1]
  2. Need q[i-1]
    1. Rerun trajectory from most recent saved step (compare which step we are at to the next “lowest” checkpoint state number)
    2. Save q[i-1]
  3. Compute adjoint contribution
  4. Add contribution to total derivative

Necessary Capabilities/Code Rewrite:

- ComputeTrajectory must be able to start at any “state” number to account for checkpoints and end at a given state
- Create a temporary vector q[i-1] so that when values are not stored during a checkpointing operation, they can still be used in computeTrajectory to go forward one step

def computeTrajectory(self, t, u, start, end)